;	Commodore 1541 / OC-118 Disk Drive Memory Map
;	V1.3	18 Jan 1995

;	Covered in this file:
;	   1541 / OC-118 Disk Drive RAM Map
;	   1541 / OC-118 Disk Drive I/O Area
;


 The following text was grabbed from "The anatomy of the 1541" by
 Lothar Englisch and Norbert Szczepanowski.
 Additions from "1541 levyasema".


Layout of the 2Kb RAM area
==========================

;	Commodore 1541 Disk Drive RAM Map
;
; The number in brackets after description is the default value after
; power-up.


; Work queue

0000		Command code for buffer 0
0001		Command code for buffer 1
0002		Command code for buffer 2
0003		Command code for buffer 3
0004		Command code for buffer 4
0005		Command code for buffer 5 (unused)

; ***

0006 - 07	Track and sector for buffer 0
0008 - 09	Track and sector for buffer 1
000a - 0b	Track and sector for buffer 2
000c - 0d	Track and sector for buffer 3
000e - 0f	Track and sector for buffer 4
0010 - 11	Track and sector for buffer 5 (unused)

0012 - 13	Disk ID, drive 0
0014 - 15	Disk ID, drive 1
0016		Header block: ID
0018		Header block: Track
0019		Header block: Sector
001a		Header block: Parity

001b		Not used (Disk Controller work)
001c		Flag for disk change, drive 0 [01]
001d		Flag for disk change, drive 1 [01]
001e		Flag for write protect sense, drive 0 [01]
001f		Flag for write protect sense, drive 1

0020		Drive 0 status (disk and step motor)
;		   bit 7: Disk drive ready (1 = No, 0 = Yes)
;		   bit 6: Read/Write head moving (1 = Yes, 0= No)
;		   bit 5: Motor on (1 = Yes, 0 = No)
;		   bit 4: Switch off motor (1 = Yes, 0 = No)

0021		Drive 1 status (disk and step motor)

0022		Current track for drive 0
0023		Flag for 1541 (0), 1540 (not 0)
;		Not used (track for drive 1)

0024		Scratch pad of GCR conversion
;		Storage for BIN -> GCR conversions

002e		Pointer for temporary storage			WORD
0030		Buffer pointer for disk controller		WORD
;		Pointer: Active buffer

0032		Pointer: *** active track
0033		Pointer: *** active sector
0034		Pointer to last converted byte
0035		Not used (decode error, GCR)
0036		Byte counter for GCR/BIN conversion
0037		Not used (bit counter)
0038		Constant 7, ID mark for start of data block
0039		Constant 8, ID mark for start of block header
003a		Parity for data buffer
003b		Not directly used
003c		Not directly used
003d		Motor flag
;		Disk drive number, on 1541 always 00

003e		Active drive (FF, if not active)
003f		Buffer number for disk controller
;		Previous work place in queue (0 - 5)

0040		Byte counter for GCR conversion
0041		Number of next work in queue (0 - 5)
0042		Destination track (to move R/W head to)		DATA
0043		Number of sectors per track for formatting	DATA
0044		Temp. work area; Scratch pad			DATA
0045		Work code temp. storage
0046		Not used
0047		Data block ID char, default 07.
;	By changing this value, a data block can be written
;	with different ID. The value must be less than 10.

0048		Counter for head movement
;		Timer: R/W head acceleration

0049		Stack pointer temp. storage [39]
004a		Step counter for head transport
;	Values 0 - 127 move the head outside and values over
;	 128 move towards the centre.

004b		? (Temp. storage)				DATA
004c		Last read sector				DATA
004d		Next sector					DATA
004e - 4f	Pointer to buffer for GCR->BIN conversion	WORD
0050		Flag for GCR format (0=BIN, 1=GCR)		DATA
0051		Current track number for formatting [FF]	DATA
0052 - 55	Storage for 4 BIN bytes for GCR coding		DATA
0056 - 5d	Storage for 5 GCR bytes				DATA
005e		Number of steps for head motor accelerating/decl. [04]
005f		accelerating/decl. factor [04]
0062 - 63	Pointer to routine for head movement [FA05]	WORD
0064		Minimum number of steps [C8]
0065 - 66	UI vector [$EB22]				WORD
0067		Flag: NMI
0068		Flag for disk initialisation			DATA
;	Automatic disk initialisation if ID MISMATCH occurred (1 = no, 0 = yes)

0069		Step size for sector division [0A]
;	Sector number interleave for SEQ files, default 10 (0A)

006a		Number of read attempts [5]			DATA
006b - 6c	Pointer: Start of Jump table for U commands [FFEA]	WORD
006d - 6e	Pointer: Start of bitmap [0400]

006f - 70	Pointer to address for M & B commands		WORD
0071		Temp. work area
0072		Temp. work area [FF]
0073		Temp. work area
0074		Temp. work area

0075 - 76	Indirect pointer [0100]

0077		Listener address (Device number + $20) [28]
0078		Talker address (Device number + $40) [48]
0079		Flag: Active listener
007a		Flag: Active talker
007b		?
007c		Flag for ATN from serial bus receiving
;		ATN interrupt
007d		Flag for ATN on serial bus active
007e		Last handled program
007f		Drive number (on 1541 always 00)
0080		Current Track number
0081		Current Sector number
0082		Channel number (Logical index)
0083		Secondary address
0084		Original Secondary address [6F]
0085		Current Data byte [3F]


0086 - 8a	Temp Results
008b - 8e	Work storage for division
;		Result, Multiply and divide
008f - 93	?

0094 - 95	Current buffer pointer				WORD
;		Pointer: Directory buffer (0204)

0096		?
0099 - 9a	Pointer: Next byte in buffer 0 [0300]
009b - 9c	Pointer: Next byte in buffer 1 [0400]
009d - 9e	Pointer: Next byte in buffer 2 [0500]
009f - a0	Pointer: Next byte in buffer 3 [0600]
00a1 - a2	Pointer: Next byte in buffer 4 [0700]
00a3 - a4	Pointer: Next byte in command buffer [0200]
00a5 - a6	Pointer: Next byte in error message buffer [02D6]

00a7 - ad	Table: Non-active channel numbers for each buffer
00ae - b4	Table:
00b5 - ba	Table: Record # low , block # low
00bb - c0	Table: Record # high, block # high
00c1 - c6	Write pointer for REL file
;		Table: next record numbers

00c7 - cc	Table: Record length for REL file
00cd - d2	Table: Side sectors

00d3		?

00d4		Pointer in record for REL file
00d5		Side sector number
00d6		Pointer to data block in side sector
00d7		Pointer to record in REL file

00d8 - dc	Directory sectors
00dd - e1	Index: Directory
00e2 - e6	Default disk drive [00]
00e7 - eb	File type (wild cards, @, closed)
00ec - f1	File type (channel)
00f2 - f7	Channel status
00f8		Flag for EOI
00f9		Current work (Buffer number)

00fa - fe	Last used table
00ff		Flag: FF = drive 0 not ready (No disk), 00 = ready
0100		Flag: FF = drive 1 not ready (No disk), 00 = ready
0101		Format marker, drive 0
;		DOS version (from track 18 sector 0)

0102		Format marker, drive 1
0103		Not used
0104 - ff	Stack area

0146		?
01ba		Buffer for GCR code

0200 - 29 	Buffer for command string
022a		Command code

;022b - 2d	Array: Logical index (LINDX)
;		Array of status bytes for each channel (secondary address)
;		Possible values:
;			FF = inactive
;			81 = opened for writing
;			41 = read/write
;			01 = opened for reading

022b		Logical index, channel 0
022c		Logical index, channel 1
022d		Logical index, channel 2

022e - 43	Last read/written byte for each channel
0244 - 49	Pointer: Last char on channel.
;		Points to the last character read/written in buffer.

024a		Type of active file
024b		String length
024c		Temp. channel number (secondary address)
024d		Current work with drive number
024e		Work area to find the best sector

024f - 50	Buffer allocated
0251		Flag: BAM changed, drive 0
0252		Flag: BAM changed, drive 1
0253		Flag for directory entry found (FF = Not found, 00 = Found)	DATA
0254		Flag for directory output
0255		Flag: Waiting for command
0256		?
0257		Last used buffer
0258		Record length
0259		Track of side sector
025a		Sector of side sector

025b - 5f	Last work (buffers)
0260 - 65	Directory sector (buffers)
0266 - 6b	File's index in directory (buffers)

026c		Counter for LED flash
;		Error Message

026d		Error LED
026e		Drive for last program
026f		sector for last program
0270		Write LINDX
0271		Read LINDX

0272 - 73	Number of blocks (temp)
0274		Length of input line
0275		Char to interpret
0276		Index: End of filename in command buffer
0277		?
0278		Number of file names
0279		?
027a - 7f	Pointer table: Filenames
0280 - 84	Track of a file
0285 - 89	Sector of a file
028a		Flag: wild cards
028c		Number of drive(s ?) to look for
028d		Flag: Looking for drive
028e		drive with last write/open error, used as default drive
028f		Flag: Found in directory
0290		Directory sector
0291		Sector for first available file
0292		Index (in directory) for first available file
0293		For the last directory entry 0
0294		Current buffer-index
0295		Counter: Files
0296		Flag: Name matching wild cards
0297		Active operating mode (R or W)
0298		Flag: Work return
0299		Pointer: Re-read error
029a		Total tracks

029b - 9c	Pointer: BAM last update
029d - a0	BAM: image sector (drives 0 and 1)
02a1 - b0	BAM image
02b1 - d4	Buffer for directory output
02d5 - f8	Buffer for error message

02f9		Flag: Don't write BAM
;		This flag is reset to zero before and after each command

02fa - fb	Number of free blocks, low byte for drives 0 ja 1
02fc - fd	Number of free blocks, hi byte for drives 0 ja 1
02fe - ff	Stepper motor sequence

0300		Buffer 0
0400		Buffer 1
0500		Buffer 2
0600		Buffer 3
0621 - 22	Formatting counter
0700		Buffer 4
07ff		End of RAM




Layout of the I/O Ports (VIA 6522)
==================================

VIA 1: 6522, port for serial bus
-------------------------------

$1800	PB, port B
$1801	PA, port A
$1802	CB, data direction port B
$1803	CA, data direction port A

$1805	Timer

    PB 7, CB2:	ATN IN
    PB 6,5:	Device address preset switches
    PB 4:	ATN acknowledge OUT
    PB 3:	CLOCK OUT
    PB 2:	CLOCK IN
    PB 1:	DATA OUT
    PB 0:	DATA IN


VIA 2: 6522, port for motor and read/write head control
------------------------------------------------------

$1C00	PB, control port B
$1C01	PA, port A (data to and from read/write head)
$1C02	CB, data direction port B
$1C03	CA, data direction port A


    PB 7:	SYNC IN
    PB 6,5:	Bit rate D1 and D0
    PB 4:	WPS - Write Protect Sense (1 = On)
    PB 3:	ACT - LED on drive
    PB 2:	MTR - drive motor
    PB 0,1:	step motor for head movement

    CA 1:	Byte ready
    CA 2:	SOE - Set Overflow Enable for 6502
    CA 3:	read/write




Disk Controller Routines
========================

This table contains the addresses and the assigned buffers:

	JOB	TRACK  SECTOR	 BUFFER
	00	  06	  07	  0300-03FF
	01	  08	  09	  0400-04FF
	02	  0A	  0B	  0500-05FF
	03	  0C	  0D	  0600-06FF
	04	  0E	  0F	  0700-07FF
	05	  10	  11	  -no ram-

If a disk controller routine is to be performed in the interrupt, one
writes the job code and the track and sector numbers of the block to be
processed (if necessary) in the appropriate memory locations. Now the
job code can be passed. This job code has a value greater than 127 (the
7th bit is set). In order to wait until the job is finished, only the
seventh bit need be tested. If this bit is cleared, the job is completed.
The disk controller can perform the following jobs:

	JOB   NAME	DESCRIPTION
	80    READ	Read sector
	90    WRITE	Write sector
	A0    VERIFY	Verify sector
	B0    SEEK	Find sector
	C0    BUMP	Bump, Find track 1
	D0    JUMP	Execute program in buffer
	E0    EXECUTE	Execute program, first switch drive on and find track

The verify job (A0) is performed automatically after writing a blcok.

If the job ends in an error then the memory location with job command
code is replaced with and error code. Here is a list of the error numbers:

	CODE	MEANING				DOS ERROR MESSAGE
	01	Everything OK			00, OK
	02	Header block not found		20, READ ERROR
	03	SYNC not found			21, READ ERROR
	04	Data block not found		22, READ ERROR
	05	Checksum error in data block	23, READ ERROR
	07	Verify error			25, WRITE ERROR
	08	Disk write protected		26, WRITE PROTECT ON
	09	Checksum error in header block	27, READ ERROR
	0B	Id mismatch			29, DISK ID MISMATCH
	0F	Disk not inserted		74, DRIVE NOT READY

  Error codes 06 and 0A do not occur on the 1541.